## Slide 1
Elevator Control System
A collective-control elevator for a 4-level PLC simulation:
the control logic and its MQTT operator interface (HMI).
HMI TEAM
operator interface
Yasin
Mevlüt
CONTROL TEAM
the control system
Ruben
Lukas
Group E
Notes: Yasin opens. Good morning - we are Group E. We built the control system for a four-level elevator together with its MQTT operator interface. Briefly introduce the four of us and the two teams: HMI team Yasin and Mevluet, control team Ruben and Lukas. Then move to the agenda.

## Slide 2
AGENDA
Two parts: the HMI and the control system
HTWG Konstanz · System Architecture · Group E
1
Part 1
The HMI & Operator Interface
What the operator sees, the MQTT interface, the status payload, the HMI app.
Yasin & Mevlüt
Part 2
The Control System
Requirements, hexagonal architecture, the SCAN logic, I/O, deployment & live demo.
Ruben & Lukas
The two halves meet at one MQTT boundary: Part 1 explains that interface, Part 2 the logic behind it.
Notes: The talk has two halves. First the HMI side - the operator interface and how it talks to the system - by Yasin and Mevluet. Then the control system itself - the logic, the I/O, and a live demo - by Ruben and Lukas. The key thing to remember: the two halves meet at exactly one MQTT boundary. Part 1 explains that interface, Part 2 the logic behind it.

## Slide 3
PART ONE
The HMI & Operator Interface
What the operator sees, the MQTT interface it speaks, and the status it reads.
Presented by Yasin & Mevlüt
Notes: Yasin: this is Part one - the HMI and the interface it speaks. We will cover what the HMI is, how it is separated from the control system, the MQTT topics, the status payload, and finally our reference HMI application.

## Slide 4
PART 1 · OVERVIEW
What we are building, and what we are not
HTWG Konstanz · System Architecture · Group E
2
The assignment
Drive a ready-made elevator simulation on a lab PLC.
Talk to the PLC as a Modbus/TCP master at a ~100 ms cycle.
Implement the full control logic for a 4-level elevator.
Division of labour
This part covers our half: the HMI / operator panel.
The controller exposes a clean, transport-agnostic interface — that's the boundary our HMI talks to.
The big picture — the HMI is our side of this interface
HMI / Operator
issues calls, reads state
›
Control System
the SCAN logic (Part 2)
›
PLC Simulation
sensors & motors (Modbus)
Notes: Yasin. Three actors: the operator and HMI on top, our control system in the middle, the PLC simulation at the bottom. Scope point: in the assignment a partner group owns the HMI, but we also built a reference HMI - that is what this Part one shows. The key idea throughout is a clean, transport-agnostic interface so the two sides stay independent.

## Slide 5
PART 1 · SEPARATION
Two Maven modules, one shared contract
HTWG Konstanz · System Architecture · Group E
3
SysArch_HMI (us)
Swing HMI — animated shaft, status & call buttons
Console HMI for debug
Depends only on the contract, Paho & the JDK.
SysArch_Control
domain/ — pure logic & model
application/ — ports + loop
infrastructure/ — Modbus, MQTT, simulation adapters
Builds a runnable fat jar.
de.htwg.sysarch.mqtt
the SHARED contract
MqttTopics
StatusMessage
EventMessage
CommandMessage
JsonCodec (Gson)
One-directional interface: every interface variable is written in one direction only. State the HMI reads flows out on status / event; commands flow in on cmd. The two never share a topic, and neither module imports the other's code.
Notes: Yasin. Two separate Maven modules - the HMI and the control system. They share only one thing: the message contract in the mqtt package, the topics and the JSON DTOs. Neither module imports the other's code. And one rule from the assignment: every interface variable flows in one direction only - state out on status and event, commands in on cmd. They never share a topic.

## Slide 6
PART 1 · MQTT
The operator interface runs over MQTT
HTWG Konstanz · System Architecture · Group E
4
Control and HMI are separate processes. They meet only at a mosquitto broker, exchanging JSON on three topics under /SysArch/E.
Topic | Direction | Payload | Retained
/SysArch/E/status | control → HMI | StatusMessage | yes
/SysArch/E/event | control → HMI | EventMessage | no
/SysArch/E/cmd | HMI → control | CommandMessage | no
Example messages
status {"level":4,"direction":"NONE","phase":"IDLE", …}
event {"type":"ARRIVAL","level":3,"detail":""}
cmd {"type":"cabin","level":3}
Resilient by design
No broker → logs to console, keeps running.
Auto-reconnect; bad commands are dropped, not fatal.
Notes: Yasin. MQTT is a lightweight publish/subscribe protocol that goes through a broker - here mosquitto on the lab server. Three topics under /SysArch/E: status and event go from control to the HMI, cmd comes back. Status is retained, so an HMI that joins late immediately gets the last state. And it is resilient - if there is no broker, the control system just logs to the console and keeps running. Then I hand to Mevluet.

## Slide 7
PART 1 · STATUS PAYLOAD
Reading a status message: fields and meaning
HTWG Konstanz · System Architecture · Group E
5
Every cycle the controller publishes one StatusMessage; the HMI renders it. Example from the demo run in Part 2 (cabin going down to level 1):
Field | Example | Meaning
level | 4 | Current floor of the cabin (1–4)
direction | DOWN | Travel direction: UP / DOWN / NONE
phase | MOVING | Control state machine phase
door | CLOSED | Door state: OPEN / CLOSED / MOVING / UNKNOWN
velocity | −100 | Speed in cm/s; sign gives direction (− = down)
emergencyActive | false | Is the emergency stop engaged?
motorError | false | Is a motor fault present? (clearable by reset)
cabinCalls | [1] | Pending in-cabin target floors
hallUpCalls | [ ] | Pending hall calls wanting to go UP
hallDownCalls | [ ] | Pending hall calls wanting to go DOWN
Field names are the JSON keys; they are identical on both sides of the MQTT contract.
Notes: Mevluet takes over. Every cycle the controller publishes one status message and the HMI just renders it. Walk the table top to bottom: level, direction, phase, door, and velocity - note velocity is signed, a negative value means going down. Then the three call lists: cabin calls, hall up, hall down. This exact example is the journey we will see live later in Part two.

## Slide 8
PART 1 · THE HMI APP
Our reference HMI
HTWG Konstanz · System Architecture · Group E
6
Graphical HMI (Swing)
Animated 4-level shaft with moving cabin & sliding doors.
Per-floor call lamps light up on pending calls.
Live read-outs: level, direction, phase, door, velocity.
Buttons: cabin & hall calls, emergency stop, reset.
Scrolling event log (arrivals, doors, alarms).
Console HMI (headless / debug)
Same MQTT contract, no GUI.
Type commands: c / u / d <1-4>, e, r, x.
Prints incoming status & events to stdout.
Handy for testing without the lab or a display.
Commands the HMI sends on /SysArch/E/cmd
{"type":"cabin","level":3}
{"type":"hall","level":2,"direction":"UP"}
{"type":"emergency","action":"engage"} (or "clear")
{"type":"reset"}
The HMI depends only on the shared contract — never on control-system code.
Notes: Mevluet. This is our reference HMI. The graphical Swing version has an animated shaft with a moving cabin and sliding doors, call lamps, live read-outs and buttons. There is also a console version for debugging without a display. When the operator presses a button it becomes one of these cmd messages at the bottom. The crucial point: the HMI depends only on the shared contract, never on control code - so the partner group could swap it for any GUI. Then I hand to Ruben for the control system.

## Slide 9
PART TWO
The Control System
Requirements, hexagonal architecture, the SCAN logic, I/O, deployment and a live demo.
Presented by Ruben & Lukas
Notes: Ruben: now Part two, the control system itself. I will cover the requirements, the hardware, the architecture, and the control logic; Lukas then takes the I/O, deployment and the live demo.

## Slide 10
PART 2 · REQUIREMENTS
The twelve control requirements
HTWG Konstanz · System Architecture · Group E
7
1
Serve 4 levels
2
Two speeds up/down + crawl + off
3
Two approach sensors per level & direction
4
A sensor marks the safe door position
5
Drive at highest speed, slow before stopping
6
Hall call with direction; stop if same direction
7
Cabin call selects the target level
8
When idle, move toward the oldest request
9
Keep direction while requests lie ahead
10
Reverse when requests remain only behind
11
Minimum dwell 6 s + door open/close time
12
Emergency stop button; resume after reset
Together these define collective control (SCAN) — the focus of this part.
Notes: Ruben. The assignment gives twelve requirements - do not read them all out. Highlight the important ones: four levels; two speeds plus crawl; the sensor that marks the safe door position; the stopping rules for hall versus cabin calls; the six-second minimum dwell; and the emergency stop. Together these define collective control, which is the next slide.

## Slide 11
PART 2 · HARDWARE
The elevator: 4 levels, 2 speeds, 5 sensors per level
HTWG Konstanz · System Architecture · Group E
8
Level 4
Level 3
Level 2
Level 1
CABIN
Travel & speeds
Level height 3.5 m · two drive speeds per direction.
v2 ≈ 1 m/s (fast) · v1 ≈ 0.1 m/s (slow) · crawl −5…5 cm/s.
Always drive at the highest safe speed, slow before stopping.
Five sensors around every level
approach lower (al) −1.5 m start slowing when going UP
safety lower (sl) −50 mm switch to crawl when going UP
reached (r) 0 mm door-safe STOP position
safety upper (su) +50 mm switch to crawl when going DOWN
approach upper (au) +1.5 m start slowing when going DOWN
Level 1 has no 'al'; Level 4 has no 'au' — terminal levels are approached from one side only.
Notes: Ruben. The physical setup. Four levels, 3.5 metres apart. Two speeds per direction - fast v2 and slow v1 - plus a crawl speed for fine positioning. Around every level there are five sensors at fixed offsets; the lower, safety and reached sensors are what drive the braking on the next slide. Note the top and bottom levels only have sensors on one side.

## Slide 12
PART 2 · ARCHITECTURE
Hexagonal architecture (Ports & Adapters)
HTWG Konstanz · System Architecture · Group E
9
The control logic knows nothing about Modbus or MQTT. It talks only to ports (interfaces); adapters on the edge do the I/O.
DOMAIN pure control logic
HMI
›
Tests
›
driving port — OperatorPanel
›
PLC (Modbus)
›
HMI sink (MQTT)
driven ports — PlcGateway · HmiGateway
Why it fits: the assignment asks for components with well-defined interfaces that can be driven from the HMI or from tests. We can swap MQTT for any transport, or the simulation for the real PLC, without touching the logic.
Notes: Ruben. Our core design decision: hexagonal architecture. The domain - the pure logic - knows nothing about Modbus or MQTT. It only talks to ports, which are interfaces; adapters on the edge do the actual I/O. That is why we can run against the simulation or the real PLC, or swap MQTT, without touching the logic - which is exactly what the assignment asks for.

## Slide 13
PART 2 · ALGORITHM
Collective control: the SCAN principle
HTWG Konstanz · System Architecture · Group E
10
Keep sweeping in one direction
Serve every request in the current direction on the way.
Stop for a cabin call, or a hall call wanting the same direction.
Continue while a request lies ahead and we are not at a terminal.
Then reverse
No requests ahead but some behind → reverse direction.
When idle, head toward the oldest pending request first.
Requests are tracked with timestamps in RequestStore.
Example sweep
L1
›
L2 ↑
›
L3 ↑
›
L4
›
L3 ↓
›
L1
Up-sweep serves L2 and L3, turns at the top (L4), then the down-sweep serves L3 — never zig-zagging.
Notes: Ruben. The algorithm is collective control, also called SCAN. The lift sweeps in one direction and serves everything on the way - cabin calls, and hall calls that want the same direction. It keeps going while requests lie ahead, and only reverses when the only remaining requests are behind it. The example at the bottom shows it serves L2 and L3 going up, turns at L4, then serves L3 going down - it never zig-zags.

## Slide 14
PART 2 · DECELERATION
Stopping precisely: approach → safety → reached
HTWG Konstanz · System Architecture · Group E
11
Going UP to a target level, three sensors fire in sequence and step the speed down so the cabin halts at the door-safe position.
−1.5 m
approach lower
V2 → V1
start slowing
›
−50 mm
safety lower
V1 → CRAWL
creep in slowly
›
0 mm
reached
CRAWL → STOP
door-safe stop
Going DOWN is the mirror image: approach upper (au) → V1, safety upper (su) → CRAWL, reached (r) → STOP. The cabin then honours the minimum dwell of 6 s plus door open/close time before departing.
Notes: Ruben. How it stops precisely. Three sensors fire in sequence and step the speed down: approach takes us from V2 to V1, safety takes us to crawl, and reached means stop - that is the door-safe position. Going down is the mirror image with the upper sensors. After stopping it holds the minimum dwell of six seconds plus the door open and close time before it leaves.

## Slide 15
PART 2 · STATE MACHINE
The controller as a finite state machine
HTWG Konstanz · System Architecture · Group E
12
IDLE
waiting for a request
›
MOVING
driving at V2
›
DECELERATING
V1 on approach
›
CRAWLING
crawl on safety
DOOR_OPENING
opening at level
›
DOOR_OPEN
dwell ≥ 6 s
›
DOOR_CLOSING
closing to depart
›
EMERGENCY
stop & hold
One cycle (~100 ms): read PLC inputs → advance the FSM → derive motor & door outputs → write outputs, publish status & events. EMERGENCY interrupts from any state and resumes after reset.
Notes: Ruben. The whole controller is a finite state machine - it is always in exactly one phase: idle, moving, decelerating, crawling, the three door phases, and emergency. Every 100 milliseconds it runs one cycle: read the inputs, advance the state, derive the motor and door outputs, write them and publish status. Emergency interrupts from any state and resumes after a reset. Now I hand to Lukas for the I/O and deployment.

## Slide 16
PART 2 · I/O MAPPING
Talking to the PLC: the Modbus I/O map
HTWG Konstanz · System Architecture · Group E
13
Codesys symbols (%QX / %IX / %QW) map to Modbus coils, discrete inputs and registers. All addresses live in one place — ModbusIoMap.
Outputs we write | Codesys
Motor up / down, v1 & v2 | %QX1.0–1.3
Open / close door | %QX1.4–1.5
Crawl speed select (−5…5) | %QW1
Reset / clear motor error | %QX0.0
Inputs we read | Codesys
Level sensors al/sl/r/su/au | %IX per level
Door opened / closed | %IX10.0–10.1
Motor ready / on / error | %IX10.2–10.4
Velocity (cm/s) | %IW6
Status — Modbus not yet wired: the controller compiles against a thin ModbusConnection port; the in-memory simulation is the runnable path today. Concrete addresses still need confirming against the live lab slave.
Notes: Lukas takes over. Modbus is the simple industrial protocol we use to talk to the PLC - we are the master, the PLC is the slave, and we poll it every 100 ms. We write coils for the motor and doors, and read discrete inputs for the sensors and registers for the speed. All addresses live in one place, ModbusIoMap, so the lab layout is easy to fix. Honest status: Modbus is not wired yet - we run against an in-memory simulation, which is also what the demo uses.

## Slide 17
PART 2 · DEPLOYMENT
Shipping to the lab server (ea-pc165)
HTWG Konstanz · System Architecture · Group E
14
Laptop
Swing HMI
MQTT → broker
‹ ›
ea-pc165 (server)
broker + control jar
control → localhost:1883
‹ ›
ea-pc111 (PLC)
elevator simulation
control → Modbus :506
Build → copy → run (deploy-control.ps1)
1.
mvn package
self-contained fat jar
2.
scp jar → server
into ~/elevator/
3.
java -jar … --sim --mqtt
runs on the server
Gotcha we hit: the server runs only OpenJDK 11, so a Java 17 jar failed with UnsupportedClassVersionError. We retargeted the whole codebase to Java 11 — 21 tests still green.
Notes: Lukas. Where it runs: the HMI is on the laptop, the broker and the control jar both run on the lab server, and the PLC is a third machine. The pipeline is build, copy, run: mvn package makes one self-contained jar, scp copies it to the server, and java runs it. One real gotcha we hit: the server only has Java 11, so our Java 17 jar failed with an UnsupportedClassVersionError. We retargeted the whole codebase to Java 11 and all 21 tests still pass.

## Slide 18
LIVE DEMONSTRATION
Watch the elevator run
1 — Start
Control jar on the server (--sim --mqtt)
Broker confirms: MQTT connected
Swing HMI on the laptop
2 — Operate
Press a cabin call (e.g. level 1)
Add a hall call mid-travel
Show SCAN: served on the way
Trigger emergency & reset
3 — Observe
Animated shaft + sliding doors
status / event on /SysArch/E/#
mosquitto_sub mirrors the JSON
Notes: Lukas drives the live demo. Start the control jar on the server and confirm the broker says connected; open the Swing HMI. Then press a cabin call, add a hall call mid-travel to show SCAN serving on the way, and trigger the emergency stop and reset. Point at the animated shaft and at the messages on /SysArch/E. If the VPN or lab is down, fall back to a local broker with the same HMI - and the next slide is a recorded trace as a backup.

## Slide 19
PART 2 · DEMO TRACE
One journey on the wire: cabin call to level 1
HTWG Konstanz · System Architecture · Group E
15
Live capture from mosquitto_sub -t /SysArch/E/# — the same FSM phases, now visible as messages.
cmd {"type":"cabin","level":1}
evt {"type":"DEPARTURE","level":4,"detail":"DOWN"}
sts L4 DOWN MOVING v=0 cab=[1]
sts L4 DOWN MOVING v=-100 cab=[1]
sts L3 DOWN MOVING v=-100 cab=[1]
sts L2 DOWN MOVING v=-100 cab=[1]
sts L2 DOWN DECELERATING v=-100 cab=[1]
sts L2 DOWN DECELERATING v=-10 cab=[1]
sts L2 DOWN CRAWLING v=-10 cab=[1]
sts L2 DOWN CRAWLING v=-5 cab=[1]
evt {"type":"ARRIVAL","level":1}
evt {"type":"DOOR_OPENING","level":1}
sts L1 DOWN DOOR_OPENING door=MOVING cab=[]
evt {"type":"DOOR_OPENED","level":1}
sts L1 DOWN DOOR_OPEN door=OPEN
evt {"type":"DOOR_CLOSING","level":1}
evt {"type":"DOOR_CLOSED","level":1}
sts L1 NONE IDLE door=CLOSED
What happens
Request
cabin call for level 1 arrives on cmd.
Depart & speed up
DEPARTURE event, then MOVING at v=-100.
Slow down
DECELERATING → CRAWLING as sensors fire.
Arrive & doors
ARRIVAL, then the full door cycle.
Idle
call cleared, back to IDLE at level 1.
Notes: Lukas. This is a real capture of one journey - a cabin call to level 1 while the cabin is at the top. Read down the left column: the call comes in, then departure, moving at full speed minus 100, then decelerating, crawling, arrival, the full door cycle, and back to idle. The right column maps each step to the exact FSM phases from Ruben's state-machine slide - it is the theory made visible on the wire. Use this if the live demo has any issue.

## Slide 20
WRAP-UP
What we delivered & what we learned
HTWG Konstanz · System Architecture · Group E
16
Delivered
Full collective-control logic for all four levels.
Clean hexagonal design; HMI fully decoupled via MQTT.
Reference Swing + console HMI; server-deployable fat jar.
21 unit tests, all green.
Lessons learned
Match the runtime early — Java 11 on the server forced a retarget.
Keep secrets out of git — credentials via -D / env, never committed.
Tooling traps: Git-Bash mangles /topics; PowerShell scripts fix it.
Ports & adapters made the simulation a first-class test rig.
Still open: wire the real easymodbus library and confirm the Modbus address layout against the live lab slave — then the same logic drives real hardware.
Thank you — questions welcome.
Notes: To wrap up: we delivered the full collective-control logic for four levels, a clean hexagonal design, an HMI fully decoupled over MQTT, and a deployable jar - with 21 tests green. Lessons learned: match the runtime early, keep secrets out of git, and watch the tooling traps. Still open: wiring the real Modbus library and confirming the lab addresses - then the same logic drives real hardware. Thank you, and we are happy to take questions.